## Slide 1
IEEE METAVERSE GRAND CHALLENGE 2026
Sustainable Smart Cities and Urban Innovation
Bus 18
A weak rural feeder, 287 electric cars, and a voltage band you are not allowed to leave.
A browser trainer that teaches operators to distrust a safety number until they have seen what it cost in service.
substation
bus 18 — the far end
Built on
IEEE 33-bus
Baran–Wu feeder
Live backward/forward
sweep power flow —
not an animation.
Md. Rifat Rahman · BUET EEE · solo entrant
rifat137710.github.io/Public
Notes: Theme: Sustainable Smart Cities and Urban Innovation. Bus 18 is a browser-based simulation trainer built on the IEEE 33-bus benchmark distribution feeder.

## Slide 2
A neural network lost to a rule from 1547
Mass EV charging on a weak feeder pulls voltage down hardest where people are furthest from the substation. Two objectives pull against each other: keep the grid legal, and get everybody charged.
Uncoordinated
Everyone charges at once.
0.319 illegal · 0.983 served
IEEE 1547 droop
Each station watches its own bus.
0.045 illegal · 0.564 served
Plain deep RL
Full state, millions of steps.
0.057 illegal · 0.265 served
SafeSAC
Network physics in the loop.
0.016 illegal · 0.554 served
SAFETY → SERVICE
0.0
0.5
1.0
Uncoordinated
Droop
Plain deep RL
SafeSAC
violation rate →
vehicles served ↑
Plain deep RL sits below and to the right of a rule written down in a standards document — beaten on safety and on service at once.
Intelligence was not the missing ingredient. The physics was.
Notes: The credibility beat. This result comes from the underlying B.Sc. thesis and is reproduced live in the browser on the public benchmark network.

## Slide 3
Six stages. You fail first.
The ordering is the pedagogy. Nobody is impressed by a solution to a problem they have not personally felt, so the learner runs the feeder — and fails — before they see a single controller.
1
You drive
Four stations, no safety layer, 287 cars. Almost nobody threads it.
2
Uncoordinated
Everyone charges on plug-in. Service without safety.
3
IEEE 1547 droop
The standard answer. Safety bought by refusing to operate.
4
Plain deep RL
The obvious modern answer, and it loses. The credibility beat.
5
Physics restored
A projection onto what the live network can survive.
6
The trap
Pick one to deploy — from the two columns a manager gets handed.
Hands-on means the world itself: grab a charging station where it stands in the village and drag it, and a real power flow re-solves across all 33 buses.
Notes: Stage 6 is a procurement table, not a simulation run. It is where the entry lands its thesis.

## Slide 4
Real physics, in a browser tab
No server, no install, no headset. Runs on a phone. Every number on screen is computed live from the benchmark network — nothing is pre-rendered.
VERIFIED AGAINST PUBLISHED VALUES
NOTHING WAS TUNED TO
Power flow
Backward/forward sweep on the radial IEEE 33-bus feeder. 288 steps per simulated day.
Voltage sensitivities
dV/dP and dV/dQ re-measured by perturbation on the live network at every control step.
The safety layer
Dykstra projection of the agent's request onto the band polytope. 0.07 ms typical.
Adaptive gamification
Controls stay locked until a stage needs them; every reveal is computed from the run that just happened.
Sustainability analytics
Line losses surfaced per driver served: 6.0 kWh coordinated against 12.0 uncoordinated.
Accessibility
Shape-coded charts, flash rate held under the WCAG limit, reduced-motion honoured, keyboard paths throughout.
0.9131 pu
model Vₘᵢₙ vs 0.913 published
202.68 kW
model loss vs 202.7 published
1.273
dominance ratio vs 1.271
66
assertions on every commit
Notes: The strong-feeder minimum voltage and loss are published Baran-Wu values that nothing in the model was fitted to.

## Slide 5
What it teaches, and how we know
The measurement that matters
Shown only violation rate and cost, engineers deploy the controller with the best safety score on the board — the one that served nobody, all day. It earns that record by never operating, and in the field you never find out, because reality does not hand you the counterfactual.
__ of __
deployed the controller
that served nobody
__ → __
concept score, out of 10
pre and post
__
System Usability Scale
(68 is average)
~20 min
end to end, in a browser,
on any device
Eight stated objectives, each tied to a stage and tested before and after.
Play it rifat137710.github.io/Public
Source github.com/Rifat137710/Public
Prior work: Safe Deep Reinforcement Learning for Vehicle-to-Grid Voltage Support in Weak Distribution Feeders — Md. Rifat Rahman and Sad Sami, BUET EEE, 2026. Cited as prior work, not submitted as the entry.
Notes: The blanks are filled from the tester study before submission.